## Slide 1: SSD-Insider: Internal Defense of Solid-State Drive against Ransomware with Perfect Data Recovery
Trubachev Ilya 818, Nazarov Konstantin 818
Gazizov Yakov 818, Oparina Daria 815

## Slide 2: Agenda
What is ransomware?
Project motivation
Examples of crypto ransomware
Effective detection
Implementation
Proposals for future work

## Slide 3: What is Ransomware?
malware that encrypts victim’s data, where the decryption key is released after a ransom is paid by the data owner to the attacker
ransomware encrypts data using strong encryption algorithms
ransomware tries to subvert standard malware defenses by using networks that utilize anonymous communication systems such as Tor
thieves collect ransom using cryptocurrency, such as Bitcoin, which is very difficult to track

## Slide 4: Project motivation
Many ransomware attacks were reported recently.
Even after obtaining the secret key, there is no guarantee the data will be recovered completely.
Even IF THE RANSOM IS PAID there is no guarantee the secret key will be obtained

## Slide 6: Examples of crypto ransomware
WannaCry
CryptoWall
TeslaCrypt (a.k.a. AlphaCrypt)
Locky

## Slide 7: Effectively detect and perfectly recover data, even when:
a user does not run any ransomware monitoring application
the OS does not execute any ransomware monitoring task
it works for an unknown OS, an unknown file system and unknown applications
it confronts previously unknown ransomwares

## Slide 8: Flash Translation Layer (FTL)
write updated information to a new empty page and then divert all subsequent read requests to its new address
ensure that newly-programmed pages are evenly distributed across all of the available flash so that it wears evenly
keep a list of all the old invalid pages so that at some point later on they can all be recycled ready for reuse

## Slide 9: Distinguishing ransomware from normal applications with similar overwriting behavior
OWIO denotes the number of overwritings for a time slice (e.g., 1 sec).
OWST is the fraction of overwritten blocks over the total number of write requests during a time window.
PWIO is the number of overwritings for a time window consisting of N time slices.
AVGWIO is the average length of continuously overwritten blocks in a current time window.
OWSLOPE is the fraction of the number of overwritings during a current time slice over the average number of overwritings over the previous time window.
IO is the fraction of the number of overwritings during a current time slice over the average number of writings over the previous time slice

## Slide 11: Achieved results
WannaCry emulator
SSD IO driver
SSD HardWare FTL
Real-time statistics
Decision engine
Verdict
On the collected data we achieved up to 80% success rate

## Slide 12: Demo

## Slide 13: Difficulties

## Slide 14: Difficulties

## Slide 15: Two sliding windows one virus

## Slide 16: Data recovery process
SSD-Insider notifies users of which suspicious behaviors are detected
if a user responds that ransomware attack is suspected, SSD-Insider’s FTL first makes an SSD read-only
replace individual mapping entries with the corresponding backup entries
status of the mapping table is rolled back to the time just before 10 seconds
reboot the system and to get rid of ransomwares using anti-virus programs

## Slide 18: Reference
Based on the research supported by Global Research Lab. (GRL) Program of the National Research Foundation (NRF) funded by Ministry of Science, ICT (Information and Communication Technologies) and Future Planning(NRF-2016K1A1A2912757)